## Slide 1: Multi-Hop LoRa Network Protocol with Minimized Latency
Reviewed by Wanarut Boonyung
4 December 2020
Dinh Loc Mai and Myung Kyun Kim
Department of Electrical and Computer Engineering, University of Ulsan, Ulsan 44610, Korea
Received: 12 February 2020; Accepted: 13 March 2020; Published: 15 March 2020
Notes: This paper propose a minimized latency multi-hop LoRa network protocol to improve on the disadvantages of LoRa protocol.

## Slide 2: Introduction
A source node wants to send the data packet to a destination node.
But a destination node is not in the wireless communication range.
data

## Slide 3: Introduction
A source node must send the data packet via intermediate nodes until reaches a destination node.
This mechanism was called the Multi-Hop.
data

## Slide 4: Introduction
The disadvantages of multi-hop are high latency and low reliability.
100 ms
500 ms
200 ms
500 ms
Total latency is 1300 milliseconds

## Slide 5: LoRa network
LoRa (Long Range) is a long-range wireless communication technology with chirp spread spectrum modulation.
It has been developed for Internet of Things (IoT) applications for long-distance and low power consumption.
Some authors proposed LoRa protocols such as LoRaWAN, LoRaBlink, DQ-LoRa and the multi-hop LoRa network with linear topology.

## Slide 6: challenge
The latency of LoRa technology is much longer than other wireless sensor network technologies.
Some multi-hop network protocol not suitable for very low bandwidths such as LoRa.
Notes: Some multi-hop network such as AODV or DSR protocol

## Slide 7: Objective
this paper proposed a minimized latency multi-hop LoRa protocol for monitoring and controlling applications over long-distance and low power consumption.
Notes: Because monitoring and controlling need minimum latency.

## Slide 8: scope of the study
Network Model
The Low Power Wide Area Network (LP-WAN) consists of one sink node and several sensor nodes for tree topology.
All nodes are assigned identification numbers (IDs) during network configuration.
All sensor nodes transmit data to a sink (s) periodically along the tree path.
Two nodes have a link, if they can transmit directly to each other.
A link on which a child and parent node communicates together is tree link.
sink
Notes: Low Power Wide Area Network model in this scope consist of 5 properties

## Slide 9: scope of the study
Protocol Model
The protocol model is based on Time Division Multiple Access (TDMA) mechanism.
All nodes in the network are assigned timeslot and channel (radio frequency) to communicate. These timeslot and channel are collision-free with the neighboring node.
In the data transmission period, the child node transmits the data packet to its parent node based on the timeslot and channel.
After receiving the data packet from all child nodes, the parent node combines all child nodes’ data with its own data and then transmits that to its parent node.
Notes: Protocol model in this scope consist of 4 properties

## Slide 10: Research methodology
The minimized latency Multi-hop LoRa protocol has 3 key features.
Distributed Aggregation Scheduling: all the nodes in the network make the schedule without all network topology information. they only know their neighbor nodes’ information.
Parallel Transmissions: the proposed protocol allows parallel non-conflicting transmission in the network. This approach reduces the latency in the network and minimizes the number of timeslots that are assigned to all the links in the network.
Minimize Packet Size: in the proposed protocol, based on the choice of parent, the packet sizes at the nodes will be minimized.

## Slide 11: Minimized Latency Multi-hop LoRa Network Protocol
The proposed protocol consists of 3 periods
The network construction period (NCP)
The upward transmission period (UTP)
The downward transmission period (DTP)
UTP
DTP
UTP
DTP

## Slide 12: Major cycles (MC)
After constructing a tree network (NCP), data transmission cycles, called major cycles (MCs), are repeated and each MC consists of UTP and DTP
UTP
DTP
UTP
DTP

## Slide 13: The upward transmission period (UTP)
UTP is a period for each node to transmit its data to the sink. It consist of N UTCs (Upward Transmission Cycles), where each LoRa nodes transmits one data to the sink.
DTP
UTP
DTP

## Slide 14: The downward transmission period (DTP)
After UTP, there is one DTC (Downward Transmission Cycle) , for the sink to transmit a command to the LoRa nodes.
UTP
DTP

## Slide 15: Example
Ch0,T5
Ch0,T4
Ch1,T3
Ch0,T3
Ch1,T4
Before NCP
After NCP

## Slide 16: Protocol packets
N: Number of LoRa nodes
In the NCP, each LoRa node joins a multi-hop LoRa network with tree topology and is assigned a channel and time slot to transmit or receive a LoRa packet.
Notes: In each cycle of the NCP, we have four timeslots, as shown in Figure 2. In NCP, it contains N cycles as shown in Figure 3.

## Slide 17: Network Construction Period (NCP)
The sink node first transmits INIT (D, SID, Cycle, N).
D is the depth of the sender node
SID is the node ID of the sender node
Cycle is the current cycle number (in which the sender node transmits the INIT packet)
N is the number of cycles in the NCP
Each node tries to receive an INIT packet from other nodes.
INIT
INIT

## Slide 18: Network Construction Period (NCP)
After receiving an INIT packet, the node adds the sender node to the parent list and chooses the optimal parent from the parent list, as explained in the next sub-section.
INIT
Parents’ A
S

## Slide 19: Network Construction Period (NCP)
JOIN
Then transmits a JOIN (D, SID, RID, UC) packet in the second timeslot (TS2) of the current cycle.
SID and RID are node IDs of the sender and receiver.
UC is a used cell assignment list (used channels and used timeslots) of its neighbors.
UC is used by the receiver to choose a timeslot and a channel which is collision-free with its neighbors.
In the NCP, each node collects UC information by overhearing JOIN, CON and ADV packets.

## Slide 20: Network Construction Period (NCP)
After receiving INIT, a node transmits the JOIN packet in TS2, but JOIN packets can collide, as shown in Figure 4a. they propose a packet collision–avoidance mechanism, as explained in the next sub-section, to avoid this.
Collisions can happen between JOIN packets and INIT packets, as shown in Figure 4b. If a node loses contention, it tries to retransmit this packet in the next cycle.

## Slide 21: Network Construction Period (NCP)
CON
After transmitting the INIT packet, if a node receives a JOIN packet from a node, this node chooses a timeslot and a collision-free channel with the UC, as explained in the next sub-section.
Then transmits a CON packet to the sender of the JOIN packet in the third timeslot (TS3) of the current cycle. The format of the CON packet is CON (D, SID, RID, Ts, Ch).
Ts and Ch indicate the assigned cell (timeslot, channel) for the receiver node to communicate with the sender node.
Parents’ A
S
Childs’ s
A

## Slide 22: Network Construction Period (NCP)
ADV
If the child node receives a CON packet from the parent node, it broadcasts an ADV packet, formatted as ADV (D, SID, RID, Ts, Ch), at timeslot TS4 to announce its cell assignment to its neighbor nodes.
ADV
ADV
ADV

## Slide 23: Example
Ch0,T5
Ch0,T4
Notes: NCP process with six nodes. At first, each node initializes its P, D, Cd and UC information, as shown in Table 1. We assume that TUTC = 5 × TS.
First, the sink node transmits INIT(0,S,0,5)
in timeslot TS1 in the first cycle (cycle 0). Nodes A and B receive the INIT packet from node S, and after that,
nodes A and B compete to transmit a JOIN packet to node S. We assume node B wins, and node B transmits JOIN(1,B,S,{}). Node A determines it lost the competition and waits until TS2 (in the next cycle) to retransmit the JOIN packet. Node S receives the JOIN packet from node B and accepts node B as its child node. Based on UC and Cd, node S decides to assign timeslot T5 and channel Ch0 to node B to communicate with node S, as explained in the next sub-section.
Node S transmits CON (0,S,B,T5,Ch0) to node B at TS3 to inform node B of its assignment. Nodes A and B receive the CON packet, B sets its parent as S and the cell assignment to P and UC, while node A adds (Ch0, T5) to its UC list. In TS4, node B broadcasts ADV (1,B,T5,Ch0) to inform its neighbor nodes of the cell assignment. After receiving the ADV packet, nodes A, C and D add (Ch0, T5) to their UC lists.
In TS4, node B broadcasts ADV (1,B,T5,Ch0) to inform its neighbor nodes of the cell assignment. After receiving the ADV packet, nodes A, C and D add (Ch0, T5) to their UC lists.
In TS1 of the next cycle (Cycle 1), node B sends INIT (1,B,1,5), and nodes A, C and E receive this packet and add node B to their parent lists.
In TS2, nodes A, C and D choose their parents as described in the next sub-section and compete to transmit a JOIN packet to the parent node. Node A wins then, sending JOIN (1,A,S,{(T5, Ch0)}) to node S. Nodes C and E determine that they lost the competition when overhearing the JOIN packet, and wait until TS3 (in the next cycle) to retransmit the JOIN packet. After receiving the JOIN packet from node A, node S accepts node A as its child and chooses TS4 and channel Ch0 as the link from A to S.
Node S transmits CON (0,S,A,T4,Ch0) to node A at TS3 to inform node A of its assignment. Nodes C, B and D overhear this packet and add (Ch0, T4) to their UC lists. Node A receives this packet and sets its parent as S, adding the cell assignment to P.
In TS4, node A broadcasts ADV(1,A,T4,Ch0) to inform the neighbor nodes about the cell assignment.
This process is repeated until the network construction is completed. Figure 6 shows the NCP process, and Table 1 shows the information maintained by each node after the NCP finishes.

## Slide 24: Packet Collision Avoidance Mechanism
LoRa’s transceiver uses the channel activity detection (CAD) mechanism to detect packets in the air.
They propose a packet collision avoidance mechanism based on CAD.
mechanism needs TCAD (CAD time) to detect packets.
TCAD = 2 × Tsym
Tsym is dependent on spreading factor (SF).
Notes: in the next sub-section, they explained a packet collision–avoidance mechanism, to avoid the collision

## Slide 25: Packet Collision Avoidance Mechanism
In TS1 and TS2 of each cycle in the NCP, each node calculates a random delay time r (r = w × TCAD).
w = random{D × CW, D × CW + CW - 1}
D is depth of this node.
CW represents the contention window size parameter.
During delay time, if the CAD mechanism detects a packet. it initiates a ‘CAD_detected’ event to inform the node. So, node will be lost contention. It will have to try to retransmit the packet in the next cycle.
r1 us
r2 us

## Slide 26: Timeslot and Channel Assignment
After receiving JOIN packet, at the parent node, Algorithm 1 chooses the latest timeslot before the timeslot in which this node communicates with its parent node.
Until timeslot is not in Cd.
Notes: in the next sub-section, they explained Timeslot and Channel Assignment

## Slide 27: Timeslot and Channel Assignment
If timeslot and channel are in Uc, change channel.
If that timeslot has not any free-channel, change timeslot.
Until timeslot or free-channel are not in Uc.

## Slide 28: Timeslot and Channel Assignment
This minimizes the number of timeslots that are used for assignments to all the links in the network.
With this algorithm, all child nodes transmit a data packet to their parent node before the parent transmits the data packet.
Thus, in one UTC, all data from LoRa nodes were forwarded to the sink node.

## Slide 29: Parent Choice Mechanism
Before the node receives a timeslot and channel assignment from the parent node, this node updates its parent based on the parent choice mechanism from the parent list as a priority, which is Rule 1.
The node has the lowest depth.
The node has the smallest number of children.
The node has the latest timeslot assigned for communication with its parent node.

## Slide 30: Parent Choice Mechanism
In Figure 8, node 6 can choose nodes 2, 3, 4 or 5 as a parent.
Based on Rule 1, node 6 chooses node 3 as its parent node
(node 3 has the lowest depth at 1, and the smallest number of children at 0).
In this case, the end-to-end latency is the lowest because node 6 will have 2 hops.

## Slide 31: Parent Choice Mechanism
In data aggregation, we assume that every node has 60 bytes as the data size.
If node 2 is chosen, it will have 240 bytes packet size,
but if node 3 is chosen it will have 120 bytes as the packet size.
To avoid exceeding the packet size, node 6 rejects node 2 as its parent to avoid exceeding the packet size. For that reason, node 6 chooses node 3, proving that Rule 1 will minimize the end-to-end latency as well as the packet size distribution
4x60 bytes
2x60 bytes

## Slide 32: REDUCE command packet
In Figure 9, we can see that two timeslots, T1 and T2, are not used; thus, to minimize the delay time and maximize the data rate, they removed these timeslots by REDUCE command packet.
Figure 10 shows data transmissions after all the nodes received the REDUCE command packet.
DTC
Notes: Furthermore, they proposed the REDUCE command packet

## Slide 33: How to insert the New Node
During the UTCs, All nodes forward a data packet to the sink node. So, the sink node can know the number of joined nodes in the network.
Base on this information, in the DTP, if the sink node determines that other nodes need to join the network, the sink node transmits the ADD command packet to notify all joined nodes to allow new nodes to join the network. Thus, before one UTC, we add one NCP cycle.
ADD

## Slide 34: How to insert the New Node
After that, in the next DTC, if the sink node determines that all nodes have already joined the network, the sink node will transmit a REMOVE_ADD command packet to notify all the nodes to remove the NCP cycle before the UTC.
remove

## Slide 35: Resynchronize Time Mechanism
If we knew the time on air, then we can estimate when the next timeslot starts, as shown in Figure 13, to resynchronize the timeslot between the child nodes and the parent nodes.
Notes: However, If we knew the time on air

## Slide 36: Resynchronize Time Mechanism
After receiving a command packet, based on Equation (1), they calculated the time on air based on the received packet size, Spreading Factor (SF) and Coding Rate (CR).

## Slide 37: Experiment Evaluation
They developed the proposed protocol using the MultiTech mDot module, which consists of a Semtech SX1272 LoRa transceiver (Semtech, Camarillo, CA, USA), and an STM32F411RET processor (STMicroelectronics, Geneva, Switzerland) based on Mbed OS.

## Slide 38: parameters
They conducted an experiment by deploying 16 nodes with the set of parameters in Table 2.

## Slide 39: performance
They measured the performance from a successful tree construction of the proposed protocol in terms of
contention window size
successful data reception ratio at the sink after tree construction
the end-to-end (E2E) delay average

## Slide 40: Scenario
The experiment was performed under the following scenario.
Scenario: nodes are deployed on the university campus area (400 m × 400 m) as shown in Figure 14, and the density of the nodes is 1 node/10,000 m2

## Slide 41: result
Figure 15 shows the percentages of joined nodes after the NCP for 16 nodes when they increase the contention window size, the percentages of joined nodes as the NCP increased.

## Slide 42: result
The number of timeslots is low. the proposed protocol can increase the LoRa data rate. The result is better than the LoRa linear multi-hop protocol because the LoRa linear multi-hop protocol needs the number of timeslots and the number of nodes in the same.

## Slide 43: result
The proposed protocol has a low E2E delay average because it uses parallel transmissions; therefore, the proposed protocol can be applied to low-latency applications.

## Slide 44: Conclusions
This protocol is more suitable for LoRa communication technology because the time they transmit a packet is much longer than with other technologies in WSNs.
In the proposed protocol, each node can reliably transmit data by eliminating data packet collisions with neighbor nodes.
The experiments show that the proposed protocol has high data reliability and low latency.
In future research, they will analyze the energy consumption of our protocol, and improve its performance in terms of energy consumption.

## Slide 45: Data Transmission in the Proposed Protocol
In each UTC, each node transmits one data packet. If the parent node receives all the data packets from its child, it combines its own data, then transmits the packet using the channel and timeslot that is assigned during the NCP.

## Slide 46: Data Transmission in the Proposed Protocol
An SX1272 LoRa transceiver has a maximum Rx buffer of 256B.
To allow data aggregation, we restrict the degree (d) and depth (m) of the tree as follows: d × m ≤ ⌊256/L⌋, where L is the size of the data generated in each node.

## Slide 47: Research methodology
The protocol uses distributed aggregation scheduling to eliminates all collisions when transmitting data.
  the reliability of data transmission is high.
The protocol uses parallel transmissions to maximize utilized channel.
  The channel utilization is increased.
The protocol uses a tree construction algorithm, which achieves a high balance load.
  All packet size of nodes are balanced.
The protocol uses a timeslot and channel assignment algorithm to support the parallel node transmit data.
  Any source nodes can send data to any destination nodes at the same timeslot.
Notes: Research methodology consist of 4 properties

## Slide 48: Data Transmission in the Proposed Protocol
d:2, m:0
d:2, m:1
d:1, m:1
d:0, m:2
d:0, m:2
d:0, m:2
d × m ≤ ⌊256/L⌋
L ≤ 256
L ≤ 256
L ≤ 256
L ≤ 256
L ≤ 128
L ≤ 256

## Slide 49: Title Lorem Ipsum Dolor Sit Amet
2017
Lorem ipsum dolor sit amet
2018
Lorem ipsum dolor sit amet
2019
Lorem ipsum dolor sit amet